Comparison of Natural Building Techniques

a partial list of wall systems by Michael G. Smith

| Technique | Materials needed | Structural properties | Thermal properties | Best applications | Advantages | Disadvantages |
| --- | --- | --- | --- | --- | --- | --- |
| Straw bale | Straw bales, sticks or bamboo for pinnng; baling twine or wire | Load-bearing or infill; good earthquake resistance | Excellent insulation; low themal mass | Exterior walls in most climates; quick, temporary structures | Goes up relatively quickly. Fairly easy to permit. Increasing pool of experienced designers/builders. | Very susceptible to moisture damage; bales must be stored carefully; unfinished building must be protected from rain. |
| Cob | Clay soil, sand, straw | Load-bearing or infill; moderate earthquake resistance | Good thermal mass; low insulation | Exterior walls in moderate or sunny climates; interior walls; ovens and hearths; benches; garden walls; greenhouses; floors | Highly sculptural; enormous design flexibility. Combines well with other materials. | Labor intensive; goes up slowly, especially in cool, moist conditions. Permitting may take persistence. |
| Adobe | Clay soil, sand, straw or other fiber | Load-bearing or infill; poor earthquake resistance | Good thermal mass; low insulation | Exterior walls in moderate or sunny climates; interior walls; ovens and hearths; domes and vaults in dry, non-earthquake regions. | Adobe blocks can be made in one place and transported. When blocks are made, wall goes up fast. Many pros in SW. | Making and storing adobe blocks takes a lot of space and dry weather. Prone to earthquake damage. |
| Rammed earth | Clay soil with high content of sand; often stabilized with cement & reinforced with steel | Load-bearing; good earthquake resistance | Very good thermal mass; low insulation | Exterior walls in moderate or sunny climates; benches and garden walls. | Contractors, engineers and permits available in CA and elsewhere. | Ver labor or machine intensive. Requires forms. Professionally built RE can be expensive and uses non-natural materials |
| Earthbags | Woven polypropylene feed sacks filled with clay soil, sandy soil, sand, or gravel | Load-bearing; foundations for other wall systems; good earthquake resistance | Very good thermal mass; low insulation (unless filled with a light fill like pumice or scoria) | Foundations for cob, straw bale, etc.; exterior walls in moderate or sunny climates; benches and garden walls; domes and vaults in dry, non-earthquake regions. | Relatively quick earth building techique. Allows for use of wide range of fill materials. | Poly bags very susceptible to UV damage; must be protected from direct sun; long-term durability unknown. |
| Technique | Materials needed | Structural properties | Thermal properties | Best applications | Advantages | Disadvantages |
| Stone | Stones; may be dry-stacked or mortared with a mixture of sand, cement, lime and/or clay | Load-bearing; foundations; poor earthquake resistance unless reinforced | Very good thermal mass; very low insulation | Foundations, basements, retaining walls; fireplaces and hearths; floors and patios; exterior walls in non-earthquake regions with mild climates. | Very durable, even in wet conditions and in contact with ground. | Very labor intensive. |
| Straw light-clay or slipstraw | Straw (or wood chips, hemp hurds, or other suitable material); clay slip | Infill | Insulation, thermal mass vary with mix; insulation can be high per thickness | Remodels; exterior and interior walls in many climates. | Walls can be any thickness. Combines well with standard stud framing or timber framing. | Requires forms, so walls generally straight. Prone to water damage. Wood requied for frame and forms. |
| Wattle and daub | Straight, flexible sticks (or bamboo); clay soil; chopped straw and/or manure | Infill | Poor insulation; low themal mass (thick plaster increases mass) | Interior walls; unheated structures such as outdoor showers, sheds, etc.; exterior walls in hot tropics | Walls can be very thin. Uncovered wattle is very decorative. | Requires lots of straight flexible sticks which can be diffcult to find. Labor intensive. Prone to water damage. |
| Clay wattle | Clay soil; long straw; sticks | Infill | Poor insulation; low thermal mass unless wall is quite thick | Interior walls; unheated structures such as outdoor showers, sheds, etc.; exterior walls in hot tropics | Walls can be very thin, curved and sculptural. | New, little-known tecnique. Requires long straw. Prone to water damage. |
| Cordwood masonry | Wood cut into short lengths; mortar may include cement, lime, clay, sand, sawdust; lime/sawdust insulation | Infill or load-bearing (round structures only); poor earthquake resistance | Good insulation; moderate thermal mass | Exterior and interior walls | Decorative. Easy to attach wooden framing and furniture. | Wood must be very dry. Tendency for wood to expand and contract, cracking mortar and creating drafts. |
| Papercrete, Fibrous cement Fidobe or Hybrid | Recycled paper pulp; sand; cement or clay soil | Infill or load-bearing | Good insulation; thermal mass varies with mix | Exterior and interior walls; floors; plasters | Very versatile techniques. Walls easily modified. | New technique. Requires a specialized mixer. Questionable water resistance. |